********************Draft********************
Hardware Testing Sdram
04/07/21
********************Draft********************

Make a copy of the working software to test on RPi3 with Catboard.

devel@mypi3-16:~/testbuilds $ rsync -avl catzip-newautofpga mypi3-21:~/

devel@mypi3-21:~ $ cd catzip-newautofpga/catzip/sw/host

Program the FPGA using config_cat

devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ sudo config_cat ../../rtl/catzip/catzip.bin

GPIO 25 not exported, trying to export...
GPIO 17 not exported, trying to export...
GPIO 22 not exported, trying to export...

OK: SPI driver loaded

Setting GPIO directions
out
out
in
Setting output to low
0
Reseting FPGA
0
1
Checking DONE pin
0
Continuing with configuration procedure
263+1 records in
263+1 records out
135100 bytes (135 kB, 132 KiB) copied, 0.0268802 s, 5.0 MB/s
Setting output to high
1
Checking DONE pin
1
Start the software that listens to local port & a remote port.

devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ sudo ./arm-netpport
Listening on port 8363
Listening on port 8364

Check the date the catzip was created using local software.

devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs version
00800014 ( VERSION) : [.!..] 20210406

Check the date the catzip was created using remote software.

devel@mypi3-16:~/testbuilds/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs -n mypi3-21 -p 8363 version
00800014 ( VERSION) : [.!..] 20210406

devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ cat wr.sh
#!/bin/bash
./arm-wbregs 16777216 0x55
./arm-wbregs 16777220 0xaa
./arm-wbregs 16777224 0x01
./arm-wbregs 16777228 0x02
./arm-wbregs 16777232 0x00010000
./arm-wbregs 16777236 0x00020000
./arm-wbregs 16777216
./arm-wbregs 16777220
./arm-wbregs 16777224
./arm-wbregs 16777228
./arm-wbregs 16777232
./arm-wbregs 16777236

A prorgram using ./arm-wbregs which is Poke & Peek to the FPGA.
devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./wr.sh
01000000 ( SDRAM)-> 00000055
01000004 ( )-> 000000aa
01000008 ( )-> 00000001
0100000c ( )-> 00000002
01000010 ( )-> 00010000
01000014 ( )-> 00020000
01000000 ( SDRAM) : [...U] 00000055
01000004 ( ) : [....] 000000aa
01000008 ( ) : [....] 00000001
0100000c ( ) : [....] 00000002
01000010 ( ) : [....] 00010000
01000014 ( ) : [....] 00020000

devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs 16777220
01000004 ( ) : [....] 000000aa
devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs 16777236
01000014 ( ) : [....] 00020000
devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs 0x01000000
01000000 ( SDRAM) : [...U] 00000055
devel@mypi3-21:~/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs 0x01000010
01000010 ( ) : [....] 00010000

devel@mypi3-16:~/testbuilds/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs -n mypi3-21 gpio 0x00010001
0080000c ( GPIO)-> 00010001
devel@mypi3-16:~/testbuilds/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs -n mypi3-21 gpio 0x00020002
0080000c ( GPIO)-> 00020002
devel@mypi3-16:~/testbuilds/catzip-newautofpga/catzip/sw/host $ ./arm-wbregs -n mypi3-21 gpio 0x00070000
0080000c ( GPIO)-> 00070000

Leds 4 & 1 on.