*********DRAFT*********
Adapting the ICOBOARD ZIPCPU
to the CATBOARD
10/30/18
*********DRAFT*********

Adding SDRAM to catzip
Starting with this version of catzip
catzip
commit 1e0dd38e890187ae3d6629fd35ddeeaad39a6701
Author: Edward Vidal Jr <develone@sbcglobal.net>
Date: Mon Aug 13 02:04:34 2018 +0000

    speechfifo not working
Using this version of learning_hdl to copy the files to add
the sdram support to catzip

commit 59da9a3ae53a03c20d516ee4c75da5597e448205
Author: Edward Vidal Jr <develone@sbcglobal.net>
Date: Wed Oct 24 16:51:00 2018 -0600

    using hardware

./config_catzip_simulation.sh

~/testbuilds/catzip_simulation/catzip
. myenv.sh
make datestamp
make autodata

~/testbuilds/catzip_simulation/catzip/rtl/catzip
. ../../myenv.sh
make clean
make cpudefs.h
make design.h
make verilated
make bin
sudo config_cat catzip.bin

~/testbuilds/catzip_simulation/catzip/sim/verilated
. ../../myenv.sh
make clean
make

~/testbuilds/catzip_simulation/catzip/sw/host
. ../../myenv.sh
make clean
make
~/testbuilds/catzip_simulation/catzip/sw/host $ ./arm-netpport

pi@mypi3-1:~/testbuilds/catzip_simulation/catzip/sw/host $ ./test_sim102218.sh
00c00010 ( VERSION) : [...)] 20181029
02000004 ( )-> 55aaaa55
02000004 ( ) : [.U.U] aa55aa55
020ffff8 ( )-> 55aaaa55
020ffff8 ( ) : [.U.U] aa55aa55
02800004 ( )-> 55aaaa55
02800004 ( ) : [.U.U] aa55aa55
028ffff8 ( )-> 55aaaa55
028ffff8 ( ) : [.U.U] aa55aa55
02c00004 ( )-> 55aaaa55
02c00004 ( ) : [.U.U] aa55aa55
02cffff8 ( )-> 55aaaa55
02cffff8 ( ) : [.U.U] aa55aa55
02f00004 ( )-> 55aaaa55
02f00004 ( ) : [.U.U] aa55aa55
02fffff8 ( )-> 55aaaa55
02fffff8 ( ) : [.U.U] aa55aa55
pi@mypi3-1:~/testbuilds/catzip_simulation/catzip/rtl/catzip $ diff wbsdram.v ~/testbuilds/xulalx25soc/rtl/wbsdram.v
66c66
<	parameter [0:0]	F_OPT_CLK2FFLOGIC = 1'b1;
---
>	parameter [0:0]	F_OPT_CLK2FFLOGIC = 1'b0;
122,123c122
<	refresh_clk <= 10'd391; // Make suitable for 50 MHz clk
<	//refresh_clk <= 10'd625; // Make suitable for 80 MHz clk
---
>	refresh_clk <= 10'd625; // Make suitable for 80 MHz clk
183c182
<	//initial	fwd_addr = 1;
---
>	initial	fwd_addr = 1;
cd ../basic
~/testbuilds/catzip_simulation/catzip/rtl/basic
make clean
make
sudo config_cat blinky.bin
sudo config_cat dimmer.bin
sudo config_cat clktest.bin
pmodtest.bin not testing.
cd ../leddigits/
~/testbuilds/catzip_simulation/catzip/rtl/leddigits
make clean
make
sudo config_cat leddigits.bin
cd ../switch_leds/
~/testbuilds/catzip_simulation/catzip/rtl/switch_leds
make clean
make
sudo config_cat switch_leds.bin
cd ../pptest/
~/testbuilds/catzip_simulation/catzip/rtl/pptest
make clean
make
sudo config_cat hellopp.bin
. Hello, World!
sudo config_cat speechpp.bin
. |===================================================================|
. | |
. | Four score and seven years ago our fathers brought forth on this |
. | continent, a new nation, conceived in Liberty, and dedicated to |
. | the proposition that all men are created equal. |
. | |
. | Now we are engaged in a great civil war, testing whether that |
. | nation, or any nation so conceived and so dedicated, can long |
. | endure. We are met on a great battle-field of that war. We have |
. | come to dedicate a portion of that field, as a final resting |
. | place for those who here gave their lives that that nation might |
. | live. It is altogether fitting and proper that we should do this. |
. | |
. | But, in a larger sense, we can not dedicate-we can not consecrate-|
. | we can not hallow-this ground. The brave men, living and dead, |
. | who struggled here, have consecrated it, far above our poor power |
. | to add or detract. The world will little note, nor long remember |
. | what we say here, but it can never forget what they did here. It |
. | is for us the living, rather, to be dedicated here to the |
. | unfinished work which they who fought here have thus far so nobly |
. | advanced. It is rather for us to be here dedicated to the great |
. | task remaining before us-that from these honored dead we take |
. | increased devotion to that cause for which they gave the last |
. | full measure of devotion-that we here highly resolve that these |
. | dead shall not have died in vain-that this nation, under God, |
. | shall have a new birth of freedom-and that government of the |
. | people, by the people, for the people, shall not perish from the |
. | earth. |
. | |
. | |
. |===================================================================|
cd ../uart/
~/testbuilds/catzip_simulation/catzip/rtl/uart
make clean
make
sudo config_cat helloworld.bin

pi@mypi3-1:~/testbuilds/catzip_simulation/catzip/sw/host $ ./sim_hw_test.sh
he date built
00c00010 ( VERSION) : [...)] 20181029
01000000 ( RAM)-> 10000001
01000004 ( )-> 10000002
01000008 ( )-> 10000003
0100000c ( )-> 10000004
01000000 ( RAM)-> 10000001
01000004 ( )-> 10000002
01000008 ( )-> 10000003
0100000c ( )-> 10000004
01000000 ( RAM) : [....] 10000001
01000004 ( ) : [....] 10000002
01000008 ( ) : [....] 10000003
0100000c ( ) : [....] 10000004
01000000 ( RAM) : [....] 10000001
01000004 ( ) : [....] 10000002
01000008 ( ) : [....] 10000003
0100000c ( ) : [....] 10000004
Turning on the 4th led
00c00008 ( GPIO)-> 00010001
Turning on the 1st led
00c00008 ( GPIO)-> 00020002
Turning on the 2nd led
00c00008 ( GPIO)-> 00040004
Turning off the leds
00c00008 ( GPIO)-> 00070000
Versions of support sopport software to
*******************************************************************************
autofpga
commit 2f443503d1edcff1a401d30207790906cb01df32
Author: ZipCPU <dgisselq@ieee.org>
Date: Sun Aug 5 20:55:25 2018 -0400

    Fixed an uninitialized error in the subdirectory string
icestorm
commit 8cac6c584044034210fe0ba1e6b930ff1cc59465
Author: Clifford Wolf <clifford@clifford.at>
Date: Mon Jul 30 16:04:04 2018 +0200

    Also install text timing databases

    Signed-off-by: Clifford Wolf <clifford@clifford.at>
arachne-pnr
commit 5d830dd94ad956d17d77168fe7718f22f8b55b33
Merge: 3a40328 9763e6e
Author: Clifford Wolf <clifford@clifford.at>
Date: Sun May 13 20:58:41 2018 +0200

    Merge pull request #115 from awygle/lm

    Add basic lm4k support (no hard IP)
yosys
commit e275692e84c935d0cdf42c2a4adf7ac949a88132
Author: Clifford Wolf <clifford@clifford.at>
Date: Sun Jul 22 18:44:05 2018 +0200

    Verific: Produce errors for instantiating unknown module

    Because if the unknown module is connected to any constants, Verific will
    actually break all constants in the same module, even if they have nothing
    to do structurally with that instance of an unknown module.

    Signed-off-by: Clifford Wolf <clifford@clifford.at>
commit ab82a886305ceec79b5516d7fc356f95a762c9fd
Author: ZipCPU <dgisselq@ieee.org>
Date: Fri Apr 20 12:49:05 2018 -0400

    Renamed the autoreload value of the ziptimer to be the interval count
verilator v3.926
commit c8e437c45cf0a9849e0a0465ecca882dbb66933a
Author: Wilson Snyder <wsnyder@wsnyder.org>
Date: Wed Aug 22 18:09:06 2018 -0400

    Version bump
The following information is from https://github.com/ZipCPU/zipcpu/blob/master/doc/spec.pdf

Introduction
 The goal of the ZipCPU was to be a very simple CPU. You might think of it as a poor manâ
alternative to the OpenRISC architecture. You might also think of it as an Open Source microcontroller. For this reason, all instructions have been designed to be as simple as possible, and the base instructions are all designed to be executed in one instruction cycle per instruction, barring pipeline stalls.1 Indeed, even the bus has been simplified to a constant 32-bit width, with no option for more or less. This has resulted in the choice to drop push and pop instructions, pre-increment and post-decrement addressing modes, the integrated memory management unit (MMU), and more
    For those who like buzz words, the ZipCPU is:
    A 32-bit CPU: All registers are 32-bits, addresses are 32-bits, instructions are 32-bits wide,
       etc.
    A RISC CPU. There is no microcode for executing instructions. All instructions are designed
       to be completed in one clock cycle.
    A Load/Store architecture. (Only load and store instructions can access memory.)
    Wishbone compliant. All peripherals are accessed just like memory across this bus.
    A Von-Neumann architecture. The instructions and data share a common bus.
    A pipelined architecture, having stages for Prefetch, Decode, Read-Operand, a combined
       stage containing the ALU, Memory, Divide, and Floating Point units, and then the final
       Write-back stage. See Fig. 1.1 for a diagram of this structure.
    Completely open source, licensed under the GPL.3

“export PATH=/home/pi/zipcpu/sw/install/cross-tools/bin:/home/pi/autofpga/sw/:$PATH”

“cd catzip”

“make clean”
“make” This creates the 2 executeables arm-netpport & arm-wbregs used to communicate with the FPGA.in files for download to FPGA
In additon compiles the
The rtl has several folders basic, uart,catzip, leddigits, pptest, switch_leds, and sdram
where *.bin files are created.
The sw/host has 2 executeables arm-netpport & arm-wbregs used to communicate with the FPGA.

├── 20180605-build.v
├── 20180605-cat.tjz
├── auto-data
│   ├── bkram.txt
│   ├── board.h
│   ├── board.ld
│   ├── buserr.txt
│   ├── clock.txt
│   ├── dlyarbiter.txt
│   ├── global.txt
│   ├── gpio.txt
│   ├── hbconsole.txt
│   ├── legalgen.txt
│   ├── main_tb.cpp
│   ├── main.v
│   ├── Makefile
│   ├── pic.txt
│   ├── pwrcount.txt
│   ├── regdefs.cpp
│   ├── regdefs.h
│   ├── rtl.make.inc
│   ├── testb.h
│   ├── toplevel.v
│   ├── version.txt
│   ├── wbuconsole.txt
│   └── zipbones.txt
├── diff060418.txt
├── doc
│   ├── Makefile
│   ├── remotefpga.odt
│   ├── remotefpga.pdf
│   ├── src
│   │   └── gpl-3.0.tex
│   ├── zipcpu.odt
│   └── zipcpu.pdf
├── Makefile
├── mkdatev.pl
├── README.md
├── rtl
│   ├── basic
│   │   ├── blinky.bin
│   │   ├── blinky.pcf
│   │   ├── blinky.v
│   │   ├── clktest.bin
│   │   ├── clktest.pcf
│   │   ├── clktest.v
│   │   ├── dimmer.bin
│   │   ├── dimmer.pcf
│   │   ├── dimmer.v
│   │   ├── Makefile
│   │   ├── notes.txt
│   │   ├── pmodtest.bin
│   │   ├── pmodtest.pcf
│   │   └── pmodtest.v
│   ├── catzip
│   │   ├── auto.mk
│   │   ├── builddate.v
│   │   ├── catzip.pcf
│   │   ├── cpu
│   │   │   ├── busdelay.v
│   │   │   ├── cpudefs.v
│   │   │   ├── cpuops.v
│   │   │   ├── dblfetch.v
│   │   │   ├── div.v
│   │   │   ├── icontrol.v
│   │   │   ├── idecode.v
│   │   │   ├── memops.v
│   │   │   ├── pfcache.v
│   │   │   ├── pipemem.v
│   │   │   ├── prefetch.v
│   │   │   ├── wbarbiter.v
│   │   │   ├── wbdblpriarb.v
│   │   │   ├── wbdmac.v
│   │   │   ├── wbpriarbiter.v
│   │   │   ├── wbwatchdog.v
│   │   │   ├── zipbones.v
│   │   │   ├── zipcounter.v
│   │   │   ├── zipcpu.v
│   │   │   ├── zipjiffies.v
│   │   │   ├── zipsystem.v
│   │   │   └── ziptimer.v
│   │   ├── cpudefs.h
│   │   ├── dbg.png
│   │   ├── design.h
│   │   ├── flashconfig.v
│   │   ├── hdr.png
│   │   ├── icozip.pcf
│   │   ├── leds.png
│   │   ├── main.v
│   │   ├── Makefile
│   │   ├── memdev.v
│   │   ├── obj-arm
│   │   │   ├── Vmain__ALL.a
│   │   │   ├── Vmain__ALLcls.cpp
│   │   │   ├── Vmain__ALLcls.d
│   │   │   ├── Vmain__ALLcls.o
│   │   │   ├── Vmain__ALLsup.cpp
│   │   │   ├── Vmain__ALLsup.d
│   │   │   ├── Vmain__ALLsup.o
│   │   │   ├── Vmain_classes.mk
│   │   │   ├── Vmain.cpp
│   │   │   ├── Vmain__Dpi.cpp
│   │   │   ├── Vmain__Dpi.h
│   │   │   ├── Vmain.h
│   │   │   ├── Vmain.mk
│   │   │   ├── Vmain__Syms.cpp
│   │   │   ├── Vmain__Syms.h
│   │   │   ├── Vmain__Trace.cpp
│   │   │   ├── Vmain__Trace__Slow.cpp
│   │   │   ├── Vmain__ver.d
│   │   │   └── Vmain__verFiles.dat
│   │   ├── pbsw.png
│   │   ├── rtcdate.v
│   │   ├── rxuartlite.v
│   │   ├── rxuart.v
│   │   ├── simple.log
│   │   ├── spio.v
│   │   ├── sw.png
│   │   ├── testmain.v
│   │   ├── toplevel.v
│   │   ├── txuartlite.v
│   │   ├── txuart.v
│   │   ├── ufifo.v
│   │   ├── wbgpio.v
│   │   ├── wbpwmaudio.v
│   │   ├── wbqspiflash.v
│   │   ├── wbscopc.v
│   │   ├── wbscope.v
│   │   └── wbubus
│   │   ├── wbconsole.v
│   │   ├── wbubus.v
│   │   ├── wbucompactlines.v
│   │   ├── wbucompress.v
│   │   ├── wbuconsole.v
│   │   ├── wbudecompress.v
│   │   ├── wbudeword.v
│   │   ├── wbuexec.v
│   │   ├── wbufifo.v
│   │   ├── wbuidleint.v
│   │   ├── wbuinput.v
│   │   ├── wbuoutput.v
│   │   ├── wbureadcw.v
│   │   ├── wbusixchar.v
│   │   └── wbutohex.v
│   ├── clktest.asc
│   ├── hexbus
│   │   ├── console.v
│   │   ├── hbbus.v
│   │   ├── hbconsole.v
│   │   ├── hbdechex.v
│   │   ├── hbdeword.v
│   │   ├── hbexec.v
│   │   ├── hbgenhex.v
│   │   ├── hbidle.v
│   │   ├── hbints.v
│   │   ├── hbnewline.v
│   │   └── hbpack.v
│   ├── leddigits
│   │   ├── leddigits.pcf
│   │   ├── leddigits.v
│   │   └── Makefile
│   ├── Makefile
│   ├── pmodleds
│   │   ├── ledbouncer.pcf
│   │   ├── ledbouncer.v
│   │   ├── ledwalker.pcf
│   │   ├── ledwalker.v
│   │   └── Makefile
│   ├── pport
│   │   ├── ppio.v
│   │   ├── pport.v
│   │   ├── ufifo.v
│   │   └── wbpport.v
│   ├── pptest
│   │   ├── hellopp.bin
│   │   ├── hellopp.blif
│   │   ├── hellopp.pcf
│   │   ├── hellopp.v
│   │   ├── linepp.bin
│   │   ├── linepp.blif
│   │   ├── linepp.pcf
│   │   ├── linepp.v
│   │   ├── Makefile
│   │   ├── speech.hex
│   │   ├── speechpp.bin
│   │   ├── speechpp.blif
│   │   ├── speechpp.pcf
│   │   └── speechpp.v
│   ├── sdram
│   │   ├── Makefile
│   │   ├── sdram.pcf
│   │   └── sdram.v
│   ├── switch_leds
│   │   ├── Makefile
│   │   ├── switch_leds.pcf
│   │   └── switch_leds.v
│   └── uart
│   ├── helloworld.bin
│   ├── helloworld.pcf
│   ├── helloworld.v
│   ├── Makefile
│   ├── notwkg_speechfifo.png
│   ├── README.md
│   ├── speechfifo.bin
│   ├── speechfifo.pcf
│   ├── speechfifo.v
│   ├── speechfifo.v.notwkg
│   ├── speechfifo.v.wkg
│   ├── speech.hex
│   └── wkg_speechfifo.png
├── sim
│   └── verilated
│   ├── automaster_tb.cpp
│   ├── byteswap.cpp
│   ├── byteswap.h
│   ├── dblpipecmdr.cpp
│   ├── dblpipecmdr.h
│   ├── hellopp.cpp
│   ├── linepp.cpp
│   ├── main_tb.cpp
│   ├── Makefile
│   ├── memsim.cpp
│   ├── memsim.h
│   ├── obj-arm
│   │   ├── depends.txt
│   │   ├── verilated.o
│   │   ├── verilated_vcd_c.o
│   │   └── xdepends.txt
│   ├── port.h -> ../../sw/host/port.h
│   ├── pportsim.cpp
│   ├── pportsim.h
│   ├── qspiflashsim.cpp
│   ├── qspiflashsim.h
│   ├── regdefs.h
│   ├── speechpp.cpp
│   ├── tags
│   ├── tbclock.h
│   ├── testb.h
│   ├── twoc.cpp
│   ├── twoc.h
│   ├── uartsim.cpp
│   ├── uartsim.h
│   ├── zipelf.cpp
│   └── zipelf.h
├── sim-err.txt

Initial testing
06/05/18

cd catzip/rtl/catzip

sudo config_cat catzip.bin This programs the FPGA

cd catzip/sw/host

./arm-netpport
Listening on port 8363
Listening on port 8364

cd catzip/sw/host

./arm-wbregs version
00001010 ( VERSION) : [....] 20180605

1st Led on
/arm-wbregs gpio 0x00010001
00001008 ( GPIO)-> 00010001

1st Led off
./arm-wbregs gpio 0x00010000
00001008 ( GPIO)-> 00010000

2n led on
./arm-wbregs gpio 0x00020002
00001008 ( GPIO)-> 00020002

2nd led off
./arm-wbregs gpio 0x00020000
00001008 ( GPIO)-> 00020000

3rd led on
./arm-wbregs gpio 0x00040004
00001008 ( GPIO)-> 00040004

3rd led off
./arm-wbregs gpio 0x00040000
00001008 ( GPIO)-> 00040000

./arm-wbregs 0x2000 0x01
00002000 ( RAM)-> 00000001
pi@pi3-5:~/catzip/sw/host $ ./arm-wbregs ram
00002000 ( RAM) : [....] 00000001
pi@pi3-5:~/catzip/sw/host $ ./arm-wbregs 0x2000 0x02
00002000 ( RAM)-> 00000002
pi@pi3-5:~/catzip/sw/host $ ./arm-wbregs ram
00002000 ( RAM) : [....] 00000002

./arm-wbregs pic
00001004 ( PIC) : [....] 00000003

./arm-wbregs ufifo
00000804 ( UFIFO) : [@?@.] 403f4000
ICOBOARD RPi

RPI_SPI_CLK H11 Pin 23 Pi icoboard

rpi_cs D4 IOT_224 Pin 26 Pi icoboard

CATBOARD RPi

CATBOARD connection to FPGA pins PMOD 2 & PMOD 3 push button switches, dip switch, and leds.

CATBOARD sw1 & sw2

CATBOARD leds

BCM11_SCLK Pin 23 CATBOARD

BCM7_CE1 Pin 26 CATBOARD

CATBOARD

2.)	The 2nd issue is the PMOD connections to FPGA are different.
3.)	Third, I do not have a Diglient PMOD 4 push button switch module.
4.)	The 4th issue is the PHASE LOCK LOOP difference.
Post on #yosys
Pin C8 is my USER_CLK comes from a 100MHz osc. It is connected to IOT_197_GBIN1 on HX8K. When I try using it for as an input to PLL I get the fatal error: bad constraint on `i_clk': no PLL at pin C8.
Can only certain pins be used as inputs to PLL?
daveshah
develonepi3: use the SB_PLL40_CORE instead of SB_PLL40_PAD variant (and REFERENCECLK in instead of PACKAGEPIN)
set_io clk_100mhz C8 #R9

set_io pmod1_1 A11 #D8
set_io pmod1_2 B12 #B9
set_io pmod1_3 B14 #B10
set_io pmod1_4 B15 #B11
# 654321 catboard # 654321 icoboard
# xxxxxx PMOD3 A # xxxxxx PMOD1 A
# xxxxxx PMOD3 B # xxxxxx PMOD1 B
# 654321 # 654321
#
set_io pmod1_7 B10 #B8
set_io pmod1_8 B11 #A9
set_io pmod1_9 B13 #A10
set_io pmod1_10 A15 #A11

CATBOARD connection to FPGA pins PMOD 2 & PMOD 3 push button switches, dip switch, and leds.

In top.v

module top(clk_100mhz, pmod1_1, pmod1_2, pmod1_3, pmod1_4, pmod1_7, pmod1_8,
  pmod1_9, pmod1_10, pmod2_7, pmod2_8, pmod2_9, pmod2_10, rpi_sck, rpi_cs,
  rpi_mosi);

input rpi_sck, rpi_cs, rpi_mosi;
rpi_sck
rpi_cs
rpi_mosi

spi_ram_slave spi_ram_slave(clk, rpi_sck, rpi_cs, rpi_mosi,
  ram_addr, ram_data, ram_wr);
module spi_ram_slave(clk, sck, cs, mosi, ram_addr, ram_data, ram_wr);
PMOD pin out on icoboard

“lrwxrwxrwx 1 root staff 34 May 18 20:10 /usr/local/bin/config_cat -> /home/pi/catboard_yosys/config_cat”

#!/bin/bash

# A script to configure Lattice iCE40 FPGA by SPI from Raspberry Pi
#
# Copyright (C) 2015 Jan Marjanovic <jan@marjanovic.pro>
#
# This program is free software: you can redistribute it and/or modify
# it under the terms of the GNU General Public License as published by
# the Free Software Foundation, either version 3 of the License, or
# (at your option) any later version.
#
# This program is distributed in the hope that it will be useful,
# but WITHOUT ANY WARRANTY; without even the implied warranty of
# MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
# GNU General Public License for more details.
#
# You should have received a copy of the GNU General Public License
# along with this program. If not, see <http://www.gnu.org/licenses/>.

echo ""
if [ $# -ne 1 ]; then
    echo "Usage: $0 FPGA-bin-file "
    exit 1
fi

if [ $EUID -ne 0 ]; then
    echo "This script must be run as root" 1>&2
    exit 1
fi

if [ ! -d /sys/class/gpio/gpio25 ]; then
    echo "GPIO 25 not exported, trying to export..."
    echo 25 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio25 ]; then
echo "ERROR: directory /sys/class/gpio/gpio25 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 25 exported"
fi

if [ ! -d /sys/class/gpio/gpio17 ]; then
    echo "GPIO 17 not exported, trying to export..."
    echo 17 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio17 ]; then
echo "ERROR: directory /sys/class/gpio/gpio17 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 17 exported"
fi

if [ ! -d /sys/class/gpio/gpio22 ]; then
    echo "GPIO 22 not exported, trying to export..."
    echo 22 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio22 ]; then
echo "ERROR: directory /sys/class/gpio/gpio22 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 22 exported"
fi

echo ""
if [ -e /dev/spidev0.0 ]; then
    echo "OK: SPI driver loaded"
else
    echo "spidev does not exist"

    lsmod | grep spi_bcm2708 >& /dev/null

    if [ $? -ne 0 ]; then
echo "SPI driver not loaded, try to load it..."
modprobe spi_bcm2708

if [ $? -eq 0 ]; then
   echo "OK: SPI driver loaded"
else
   echo "Could not load SPI driver"
   exit 1
fi
    fi
fi

echo ""
echo "Setting GPIO directions"
echo out > /sys/class/gpio/gpio25/direction
cat /sys/class/gpio/gpio25/direction
echo out > /sys/class/gpio/gpio22/direction
cat /sys/class/gpio/gpio22/direction
echo in > /sys/class/gpio/gpio17/direction
cat /sys/class/gpio/gpio17/direction

echo "Setting output to low"
echo 0 > /sys/class/gpio/gpio25/value
cat /sys/class/gpio/gpio25/value

#echo ""
#echo "Please reset the iCE40 FPGA board"
#echo "Press any key..."
#read

echo "Reseting FPGA"
echo 0 > /sys/class/gpio/gpio22/value
cat /sys/class/gpio/gpio22/value
echo 1 > /sys/class/gpio/gpio22/value
cat /sys/class/gpio/gpio22/value

echo "Checking DONE pin"
cat /sys/class/gpio/gpio17/value

echo "Continuing with configuration procedure"
dd if=$1 of=/dev/spidev0.0

echo -e "\x0\x0\x0\x0\x0\x0\x0" > /dev/spidev0.0

echo "Setting output to high"
echo 1 > /sys/class/gpio/gpio25/value
cat /sys/class/gpio/gpio25/value

echo "Checking DONE pin"
cat /sys/class/gpio/gpio17/value

“cd otl-icoboard-pmodoledrgb-demo/stream-tool/”

“ffmpeg -f v4l2 -i /dev/video0 -s 96x64 -f rawvideo -pix_fmt rgb565 - | ./stream-tool”